%varphi_1 ( t ) %varphi_2 ( t ) bar a_B ^%tau bar a_B ^n bar v_B A B C bar a_{C/B} ^n bar a_{C/B} ^n bar v_{C/B} Velocity and Acceleration of Mechanical Finger

y

x
z

left lbrace alignl { binom {V_B % = % %omega _1(t) l_AB} {V_{C/B} % = % %omega _2(t) l_BC} } right none left lbrace alignl { binom {a_B ^%tau % = % %varepsilon _1(t) l_AB} {a_B ^ n% = % %omega_1^2(t) l_AB} } right none left lbrace alignl { binom {a_{C/B} ^%tau % = % %varepsilon _2(t) l_BC} {a_{C/B} ^ n% = % %omega_2^2(t) l_BC} } right none

Velocity:

left lbrace { binom {V_C ^x % = % V_B ^x % + % V_{ C/B } ^x} {V_C ^y % = % V_B ^y % + % V_{ C/B } ^y} } right none

left lbrace { binom {V_C ^x % = % V_B sin%varphi_1(t) % + % V_{ C/B } sin%varphi_2(t)} {V_C ^y % = % V_B cos%varphi_1(t) % + % V_{ C/B } cos%varphi_2(t)} } right none

V_c % = % sqrt{ (V_c ^x)^2 % + % (V_c ^y)^2 } % = %

% = % sqrt{ V_B^2 [sin%varphi_1^2(t) % + % cos%varphi_1^2(t)] % + % 2V_B V_{ C/B } [ sin%varphi_1(t) sin%varphi_2(t) % + % cos%varphi_1(t) cos%varphi_2(t)]% + % V_{C/B}^2 [sin%varphi_2 ^2(t) % + % cos%varphi_2^2(t)] }

% = % sqrt{ V_B^2 % + % 2V_B V_{ C/B } cos(%varphi_1(t) - %varphi_2(t)) % + % V_{C/B}^2 }

Acceleration:

left lbrace { binom {a_C ^x % = % (a_B ^%tau)^x % + % (a_B ^n)^x % + % (a_{ C/B } ^%tau)^x % + % (a_{ C/B } ^n)^x} {a_C ^y % = % (a_B ^%tau)^y % + % (a_B ^n)^y % + % (a_{ C/B } ^%tau)^y % + % (a_{ C/B } ^n)^y} } right none

left lbrace { binom {a_C ^x % = % a_B ^%tau sin%varphi_1(t) % - % a_B ^n cos%varphi_1(t) % + % a_{ C/B } ^%tau sin%varphi_2(t) % - % a_{ C/B } ^n cos%varphi_2(t)} {a_C ^y % = % a_B ^%tau cos%varphi_1(t) % + % a_B ^n sin%varphi_1(t)% + % a_{ C/B } ^%tau cos%varphi_2(t) % + % a_{ C/B } ^n sin%varphi_2(t)} } right none

a_c % = % sqrt{ (a_c ^x)^2 % + % (a_c ^y)^2 } % = %

% = % left [ [(a_B ^%tau)^2 % + % (a_B ^n)^2 % + % (a_{C/B} ^%tau)^2 % + % (a_{C/B} ^n)^2][sin%varphi_1^2(t) % + % cos%varphi_1^2(t)] % + % (a_B ^%tau) (a_{C/B} ^%tau)[cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % (a_B ^%tau) (a_{C/B} ^n)[sin(%varphi_2(t) - %varphi_1(t))] % + % (a_B ^n) (a_{C/B} ^%tau)[sin(%varphi_1(t) - %varphi_2(t))] % + % (a_B ^n) (a_{C/B} ^n)[cos(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

% = % left [ [(a_B ^%tau)^2 % + % (a_B ^n)^2 % + % (a_{C/B} ^%tau)^2 % + % (a_{C/B} ^n)^2] % + % [a_B ^%tau a_{C/B} ^%tau % + % a_B ^n a_{C/B} ^n][cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % [a_B ^n a_{C/B} ^%tau % - % a_B ^%tau a_{C/B} ^n][sin(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

Conclusion
After substituting the linear velocities and accelerations with their angular variants, we obtain the following.

For any point from A to B (change l_AB accordingly):

V_B % = % %omega_1 l_AB

a_B % = % l_AB sqrt{ %varepsilon_1^2 % + % %omega_1^4 }

For any point from B to C (change l_BC accordingly) :

V_c % = % sqrt{ (%omega_1 l_AB)^2 % + % 2%omega_1 l_AB %omega_2 l_BC cos(%varphi_1(t) - %varphi_2(t)) % + % (%omega_2 l_BC)^2 }

a_c % = % left [ [(%varepsilon_1 l_AB)^2 % + % (%omega_1^2 l_AB)^2 % + % (%varepsilon_2 l_BC)^2 % + % (%omega_2^2 l_CB)^2] % + % [%varepsilon_1 l_AB %varepsilon_2 l_BC % + % %omega_1^2 l_AB %omega_2^2 l_BC][cos(%varphi_1(t) - %varphi_2(t))] right none % + %
left none % + % [%omega_1^2 l_AB %varepsilon_2 l_BC % - % %varepsilon_1 l_AB %omega_2^2 l_BC][sin(%varphi_1(t) - %varphi_2(t))] right] ^ {1 over 2}

%varphi_1 ( t ) A Force Analysis of Mechanical Finger

y

x
z
bar R_21 ^y

bar R_21 ^x

C B

B P bar M_R2

%varphi_2 ( t ) bar B_1 bar B_2 bar M_R1

bar R_12 ^y

bar R_01 ^x bar R_12 ^y bar G_2

bar G_1
bar R_01 ^y